Study And Research On The Stability Of The Prime Physical Properties Of A High Technology, Polyamide Fabric Manufactured Using Smart Textiles, For Extreme, Athletic Usage.

Manos Psakis, Basilis Koskoris, Athanasia Tsatsarou, Georgios Priniotakis

Abstract

In this essay, the stability of the prime physical properties of a high technology, poly-amide fabric manufactured for extreme, athletic usage during washing cycles was tested. To this end, it was obtained a substantial quantity of Meryl Nateo, a fabric consisting of specially manufactured 100% polyamide microfibers. The material was divided into four main samples one of which was kept in its original state for comparison reasons. The other two samples were treated with one and five repeated hand-wash cycles according to the manufacturer’s instructions, while the fourth was washed using an industrial-grade, washing machine. After leaving the samples in a controlled environment for 24 hours to relax, each of them was tested with two different pairs of measurements; one to determine the state of their structure after the washing cycles and another to measure the state of their primary physical attributes. With the acquired measurements we can identify the extent of the structural alterations that occur to the samples due to the wash-cycles, and how these alterations influence the key attributes of the fabric and how using the smart textiles technology influences and affects the primary physical properties giving great potentiality. Thus, someone can extract specific information regarding the fastness of the physical behavior of the fabric during maintenance processes and obtain more generic data on the longevity behavior of the specific manufacturing technology used as opposed to other industrial methods like lamination.

Introduction

The following essay deals with the endurance and longevity of new, micro-fiber based, professional athletic fabrics and apparel. In the beginning of the article, there is a brief section providing historical data regarding the evolution of athletic wear from their early forms up until today. The following paragraphs reference the most commonly used synthetic fibers in today’s sportswear and the techniques used in their manufacturing process. The text moves on to referencing some of the key fabrics made by the aforementioned fibers and describing the principle, generic way these fabrics aid in athletic exercise. The outline of the specific mechanics on each of the referenced fabrics is also presented separately to facilitate better understanding on the different approaches that have been made to ensure comfort to the athlete. The next section deals with the measurement process followed; the preparation of the samples, as well as individual details on each of the testing methods used are given as well as the complete obtained results. The final chapter of the essay discusses the key points of the measurements, along with observations on the testing methods, general summarizing and conclusions on the obtained values plus a discussion point on the usage and development of present manufacturing technologies.

Sportswear Evolution

Professional athletic apparel and sportswear – the term used in its verbatim form-   have a surprisingly short history when directly compared to the history of sports and athletics themselves. Even though it is well documented that people throughout the world engaged in organized sporting activities as early as the 8th century B. C., appropriate pieces of clothing were virtually non existent prior to the beginning of the 20th century. It was at that time (late 1920’s) that the first article of clothing that augmented the performance of athletes –albeit in a passive form - came, in the form of the “Polo Shirt”. From that point on, specialized athletic wear have been slowly but steadily evolving up until the mid 50’s; the wide use of the –then- new, synthetic fibers in clothes like nylon and polyester helped to dramatically improve the physical properties of sportswear, primarily enhancing their level of comfort.

In the following decades (1980’s and a1990’s), the sporting apparel products underwent a more dramatic change; from passively aiding pieces of clothing they were slowly transformed into high-tech, specialized pieces of apparel that could actively benefit the athlete performing athletic activities. Newly made fabrics, made from layers of extremely light, synthetic materials and sometimes coated with special laminations, could rapidly siphon humidity and sweat away from the body and even reduce muscle fatigue by absorbing bounces and shocks; properties which made them ideal for use in sports. As the textile technology advanced so did the properties of these fabrics; today’s research and development in textile engineering and especially in the synthetic fiber manufacturing field have produced specialized fibers that actually hold the key properties that are inherent to the produced fabric, thus eliminating the use of costly and not-permanent post-production laminations and chemical processes to the manufactured clothing.

High-Technology Materials, Their Structure and Their Function

Modern athletic apparel and professional sportswear continue to rely heavily on synthetic fibers, though they are sometimes mixed with natural fibers like cotton. The fibers which are widely used in the area of sporting apparel manufacturing are polyester –in a 90% percentage, polyamide (nylon), acrylic, lycra and spandex. The manufacturing process depends on the excellent physical and chemical properties of these fibers (low drying times, low shrinkage, low moisture absorption, high elasticity, superior comfort) however they are rarely used in their simple, elongated tubular fiber form. Through processing, the cross-section of the fibers is molded to specialized shapes and patterns that accentuate the physical properties of the fibers, enabling them to perform more efficiently.

The bulk of the manufactured fibers are produced mainly in the form of micro-fibers. In this micro-fiber form, the aforementioned synthetic fibers can be used in greater number within a constant yarn cross-section, thus enabling the fibers to actively determine the physical and chemical properties of the produced yarn and clothing article respectively, and at the same time keep the total weight of the produced fabric to a minimum. Using the micro-fiber form also improves the total elasticity, “breathability” and smoothness of the finished articles of clothing, thus improving greatly the overall comfort of the finished product.

Massively produced athletic apparel and sportswear however are widely identified by specific brand names, rather than the commercial names of the synthetic fibers that form them, or the technology with which these fibers are manufactured. Commonplace brand names in the professional sportswear field include CoolMax from DuPont, Sphere Tech from Nike and Meryl SkinLifE from Nylstar, which itself is part of a greater line of specialized, synthetic fabrics named Meryl ActiSystem. The main principles behind the physical properties and behavior of these fabrics lie in the form and density of the synthetic fibers used within the cross-section of the yarns; the specialized shape of the micro-fibers cross-section in conjunction enables the fabric to actively try to sustain equilibrium between the humidity and temperature of the body and the environment. When a substantial increase in either of theses factors (temperature and moisture) occur during the athletic activity, the fibers of the fabric transfer the excess moisture and heat away from the body to the outer layer of the article. This process, commonly referred to as “moisture wicking”, is achieved via either the shape of the cross-section of the fibers used, their inherent ability to expand and contract when found in environments of extreme humidity and heat or their ability to alter the structure of the whole fabric to permit greater air-permeability. The later abilities are already being used as guides in the manufacturing of “smart textiles”; by electronically monitoring the changes occurring to the fibers during athletic exercise, a smart textile fabric can automatically adjust the density of its structure in order to actively improve the performance of the athlete by keeping his/her body cool and dry. In the case of high-density, elastic materials, smart fabrics can use small, controlled electric charges to tighten or loosen the pressure that the fabric applies to muscles, thus reducing muscle-fatigue, uncontrolled muscle flexing and bouncing. [1],

CoolMax

The CoolMax family of fabrics was the first to use polyester fibers with special shape to achive the “moisture wicking” effect. The fibers have 4 channels running along the entire length of their surface, while the core of the fibers is semi-hollow in a “C” shape.[2],[3] These characteristics of the morphology of the fibers enable them to create a capillary effect; the excess moisture is transferred –without being absorbed- across the channels from the inner layer of the fabric to the outer layer where it is spread in a wide surface to facilitate quick evaporation. At the same time, the shape of the cross-section of the fibers used in CoolMax greatly improves the air-permeability of the fabric and is mainly responsible for the fabrics’ natural resistance to pill formation on its surface, benefiting the overall resistance of the fabric to strain.[4],[5]

Sphere Tech

Sphere Tech fabrics also use specialized polyester fibers, branded as Moisture Respondent Transformable fibers or MRT. [6] In this case however, the cross-section of the fibers is not responsible for the physical properties of the fabric. MRT fibers, as their name clearly states, have the unique ability to expand or contract at will depending on the temperature and moisture conditions surrounding them.[7] When placed in a high humidity environment, MRT fibers contract so that excessive moisture and heat can be siphoned rapidly away form the human body. On the contrary, when placed in extremely cold and dry conditions the fibers expand so that the structure of the overall fabric becomes denser, thus preventing the temperature of the athlete to drop sharply.[8]

Meryl Actisystem

The widest and most diverse family of specialized, professional athletic fabrics is Meryl Actisystem.[9] Comprising of 7-8 different kinds of fabrics, all manufactured using specially designed, ultra-fine polyamide micro-fibers, each of the Meryl Actisystem fabrics addresses different problems that arise during sporting activities. The high fiber count of special polyamide micro-fibers in the yarns’ cross-section, in conjunction with the physical properties inherent in polyamide and the mixing with chemical agents during the production process of the fibers give Meryl Actisystem fabrics their unique and varied properties; The density of the extremely thin micro-fibers is high enough to absorb large amounts of U. V. radiation, while at the same time keeping air-permeability and overall comfort at extremely high levels. While not capable of direct “moisture wicking”, the polyamide micro-fibers used in Actisystem products are relatively non-absorbant and have a tendency to rapidly reject excess of sweat away from the human body. Additionally, in Meryl SkinlifE fabrics, a special chemical agent is mixed with the polyamide polymer that the fibers consists of, that has the ability to keep the bacterial growth on the skin of the athlete in nominal levels and also prevent them from migrating to the fabric, thus enhancing comfort and longevity of the fabric. [10,11,12]

Experimental

As stated, the purpose of this article is to determine the longevity of some of the key properties of professional athletic apparel. To this extent, a substantial amount of pre-dyed, 100% polyamide, knitted fabric of the Meryl Actisystem brand –and specifically under the Meryl Nateo commercial name. The original piece of fabric was divided into 3 equal testing samples, approximately 50 cm wide by 20 cm long each. One of the samples was kept in its original state to facilitate later testing comparison while the other two samples underwent a series of washing cycles, according to the instructions of the manufacturer. The second sample was washed one time, while the third one underwent 5 consecutive wash cycles. Both original and washed fabric samples were left in a controlled environment (22,5o C temperature and 66% moisture percentage) for 24 hours to dry and acquire nominal levels of moisture and temperature. After acclimating the 3 samples, a set of 4 test measurements were performed on each of the samples; two of which were performed to determine the state and alterations on the fabrics’ structure and the other two to determine the state and durability of two of the prime physical properties of the fabric (moisture absorption and air-permeability). Throughout the duration of the measurements, temperature and humidity levels in the laboratory were kept to the aforementioned nominal values.

Results and discussion

Determining the weight of the fabric with nominal moisture absorption according to ISO standards.

For the purposes of this set of measurements, the 3 samples were placed consecutively on a special, rough surface. The samples were placed in such a way so that they were not stretched, creased or folded in any way. With the use of a certified, SDL round weight cutting equipment, 5 specimens were randomly cut from the whole surface of each of the samples. The specimens were individually weighed in an electronic, 5-digit precision scale. After the completion of the measurements a median for each of the samples was produced, rounded up to the first decimal. The measurements obtained were as follow.

| ( | Sample 1 (Original State) | Sample 2 (1 Wash Cycle) | Sample 3 (5 Wash Cycles) |
| --- | --- | --- | --- |
| 1. | 2,3520 | 2,4765 | 2,4307 |
| 2. | 2,3398 | 2,4890 | 2,4860 |
| 3. | 2,3702 | 2,4825 | 2,4751 |
| 4. | 2,3853 | 2,4387 | 2,4817 |
| 5. | 2,3548 | 2,4871 | 2,4804 |
| Median (gr/m2) | 236,0 | 247,5 | 247,1 |

Table-1 Measurements of the Weight of the Fabric with Nominal Moisture Absorption

Determining the density of rows and columns in knitted structures according to ISO standards.

For the purpose of this set of measurements, the 3 samples were placed consecutively in a smooth, wide surface, under conditions of excellent lighting. The samples were placed in such way so that they were not stretched, creased or folded in any way. With the use of a special, certified “James Heal” magnification lens two sets of 5 measurements for each of the 3 samples were taken; one set to determine the rows’ yarn density and the other to determine columns’ yarn density. The measurements were done by manually counting the number of yarns found in any direction, within a space of 2 centimeters. After the completion of the measurements, a median for each of the sets was produced, referring to a ratio of yarns per one centimeter, rounded up to the nearest non-decimal number. The results obtained were as follow.

| ( | Sample 1 (Original State) | Sample 2 (1 Wash Cycle) | Sample 3 (5 Wash Cycles) |
| --- | --- | --- | --- |
|  | Columns | Rows | Columns | Rows | Columns | Rows |
| 1 | 34 | 48 | 34 | 49 | 34 | 49 |
| 2 | 34 | 47 | 34 | 49 | 35 | 49 |
| 3 | 34 | 48 | 34 | 48 | 35 | 50 |
| 4 | 34 | 48 | 35 | 48 | 34 | 49 |
| 5 | 34 | 48 | 34 | 49 | 34 | 49 |
| Median (yarns/cm) | 17 | 24 | 17 | 24 | 17 | 25 |

Table-2 Measurements of the Density of Rows and Columns in Knitted Structures

Determining the moisture-absorption capability of knitted fabrics according to ISO standards.

For the purpose of this set of measurements, the 3 samples were placed consecutively in a smooth, wide surface, under conditions of excellent lighting. The samples were placed in such way so that they were not stretched, creased or folded in any way. Special care was taken in the orientation of the fabric; with its inverted side looking up, and its good side contacting the surface.  A generic, laboratory syringe was filled with pure water and consecutively was used 5 times on each of the samples to drop a single droplet of water on the inverted side of the samples from a height no more than 5 centimeters from the fabric’s surface. A high precision, digital stop-clock was used to clock the exact time needed for the full absorbance of the droplet. The measurements were produced in seconds, and after the completion of the process, a median for each sample was produced. In the case of the absorbance time being less than 5 seconds the median is presented as “below 5”, according to the directions of the ISO standard used. The results obtained are as follow.

| ( | Sample 1 (Original State) | Sample 2 (1 Wash Cycle) | Sample 3 (5 Wash Cycles) |
| --- | --- | --- | --- |
| 1. | 4 | 3 | 32 |
| 2. | 4 | 3 | 36 |
| 3. | 4 | 3 | 31 |
| 4. | 4 | 4 | 33 |
| 5. | 3 | 3 | 31 |
| Median (sec) | <5 | <5 | 33 |

Table-3 Measurements of the Moisture-Absorption Capability of Knitted Fabrics

Determining the air-permeability of knitted fabrics by ISO standards.

For the purpose of this set of measurements, the 3 samples were placed consecutively in specialized electronic equipment capable of measuring air-permeability of knitted and/ or woven fabrics. The machine was calibrated individually for every sample to a pre-pressure level of 0,098 Pascal and the level of sensitivity was set to level 3 –from a scale of 1 to 6. Both of these settings were obtained after testing the machine with random pieces of the original fabric. Consecutively, each of the samples was placed in the machine’s measuring surface in such way so that they were not stretched, folded or creased and later locked into place using the appropriate locking mechanism of the machine. The air-permeability testing machine was then turned on giving the precise value of the amount of air pressed through the fabric’s surface. The equipment was used 5 times on different areas of each of the samples so as to obtain a thorough set of measurements. After the process was completed, a median for each sample was produced, rounded up to the second decimal. The results obtained were as follow.

| ( | Sample 1 (Original State) | Sample 2 (1 Wash Cycle) | Sample 3 (5 Wash Cycles) |
| --- | --- | --- | --- |
| 1. | 8,88 | 8,40 | 8,30 |
| 2. | 8,40 | 8,72 | 8,08 |
| 3. | 8,69 | 8,29 | 8,01 |
| 4. | 8,92 | 8,15 | 8,27 |
| 5. | 8,36 | 8,07 | 7,98 |
| Median (cm3/cm2/sec) | 8,65 | 8,33 | 8,13 |

Table-4 Measurements of the Air-Permeability of Knitted Fabrics

With the completion of the measurements multiple points of interest appear. As stated in the previous section, the first couple of measurements regard fabric weight and structural form. Since the Meryl Techno is a high-tech, professional athletic fabric whose properties heavily depend on the alignment and density of the polyamide micro-fibers, it is inevitable that any major alterations to these factors will greatly affect the key properties of the fabric.

Having established this connection, we move on to interpreting the obtained values of this first set of measurements. As far as the fabric’s weight is regarded, the original sample starts off as a light-weight fabric, ideal for athletic purposes. The successive washing cycles that both the second and third sample underwent only showed a slight –though measurable- increase of the overall weight. Specifically, the increase –which is of a percentage of 4, 7% compared with the original sample’s median weight- becomes apparent even from the second sample that underwent a single wash cycle. However, though this change clearly implies a tendency of the fabric to shrink as far as commercial standards go, this increase is not substantial nor is it wide enough to change the lightness of the fabric. This becomes even more apparent when comparing the third sample with the previous two; the individual measurements as well as the median weight show minute increase compared with the second sample –about 0,0002%-, and practically the same percent of weight increase when compared to the first, original sample. Additionally, it appears that even though the first wash cycle affected the weight of the fabric, subsequent washings did not have any measurable effects.

The points discussed above are more evident when interpreting the obtained values regarding the density of the yarns in the samples’ structure. The original sample shows a mid-density fabric -17 yarns per centimeter in the rows direction, and 24 yarns per centimeter in the columns direction- which justifies the light-weightiness of the fabric. The values obtained from the second sample, clearly show a slight tendency of the fabric to shrink, even though the medians for both rows and columns remain the same with the original sample. This tendency is even more apparent in the third sample where the yarn count in the columns’ direction is increase by one yarn per centimeter, while in the rows’ direction the same shrinkage tendency starts to appear when looking at individual measurements. The shrinkage tendency is not great, and is fully aligned with the tendency of the fabric to gain weight as observed in the previous paragraph. Overall structural behavior of the samples shows high endurance of the material to the washing cycles which will logically be translated into stability of the key properties of the fabric.

Having established the endurance of the fabric’s structural stability, we move on to the next set of measurements, regarding the key physical properties of the material; moisture absorption and air permeability. The most interesting aspect of this set of measurements comes when interpreting the moisture absorption capability of the fabric. In its original, unwashed state, the first sample appears highly absorbent, allowing the droplet of water to rapidly move from the inner surface to the outer one. The median value of absorption ability of the fabric is below 5 seconds, thus classifying the fabric as excellent. The same applies to the second sample as well; the shrinkage of the yarns causes more micro-fibers to appear in the same area of fabric, thus achieving the capillary effect more efficiently. When looking at the obtained values, this translates as a 1 second reduction in the time needed to absorb the droplet. However, the third sample shows a great increase in the time needed to absorb the droplet; the estimated median is 33 seconds, which is equivalent to an 88% increase when compared to median of the other two samples. Taking under consideration the values obtained by the previous two sets of measurements –the ones regarding the structural integrity of the fabric- the explanation of this effect is dual in nature. While in the second sample, the shrinkage tendency the fabric shows, has a positive effect as far as absorption goes, in the third sample, where that tendency appears completed, the shrinking of the fabric probably causes the yarns of the fabric to approach one another in such a dense way that the opposite effect happens; the absorption surface of the yarns is reduced, thus taking more time for the specific sample to absorb the droplet. It should also be taken under consideration that the third sample has undergone 5 consecutive washing cycles meaning that any possible excess of dye still left on the surface of the fabric has been completely removed. It is well known that molecules excess of dye left on fabrics tend to form chemical bonds with the molecules of water, thus helping in some way the absorption capability of the fabric itself. The removal of such molecules during the washing cycles may also have caused the sharp increase in the time needed for the third sample to absorb the droplet of water.

Some of these aspects are also evident when analyzing the final set of measurements, regarding the air-permeability property of the samples. The original sample gives a median of 8, 65 cubic centimeters of air per square centimeter of fabric per second, which is in accordance with the sample’s structural characteristics –medium density of yarns- and shows a satisfactory air permeability property of an athletic fabric. The second sample –in which the shrinkage effect is starting to appear- shows a slight decrease of the amount of air able to move through the fabric’s structure. The difference between the two median values is estimated around 0, 23%, which is enough to give the second sample the same satisfactory classification as the first one. When observing the third sample’s measurements –where the shrinkage effect is almost completed- the decrease in airflow is even more evident; there is a 6, 39% decrease in airflow when comparing the medians of the first and third sample, and a 2, 46% decrease when comparing the second and third median values. Although the classification of the ability of the third sample to permit air to flow through its structure remains the same as the previous’ this decrease is in accordance with the conclusions made in the last paragraph; it indeed appears that after 5 washing cycles, the structure of the third sample has become more dense so that air and water can move with greater difficulty through the mass of the sample. However, the overall behavior of all three samples has remained steady throughout this set of measurements.

Conclusions

Summarizing the conclusions drawn individually for every set of measurements, it becomes apparent that modern athletic-purpose fabrics show remarkable behavior during the processes of maintenance (washing). Their structure remains almost unaltered during the washing cycles and any occurring alterations do not decrease the effectiveness of the fabrics’ key properties. In our measurements there was a substantial decrease in performance when it came down to measuring the third sample, however it should be taken under consideration that Meryl Techno fabric which was examined throughout this document is not advertised nor manufactured as a top performance “moisture wicking” material. Its key features are light weightiness and superb air-permeability, where in both fields all of the samples excel. Furthermore the new breed of high-tech fabrics –of which Meryl Techno is part of- that depend on specialized mico-fibers as far as physical properties go are obviously a great improvement on older technologies like lamination and chemical coating. Both of the later techniques, used in the past to imbue materials with special properties, have shown time and again that are easily susceptible to the strain of washing, and once the coating is removed through the process of constant washing cycles all that remains is a plain fabric, losing all of its special properties. In the case of new fabrics, where the properties of them depend solely on the micro-fiber structure, not only their longevity is far more superior but also the production costs are reduced dramatically since there is no further need for costly and unstable post production, chemical finishing processes.

Further studies on this subject can easily link the new technology micro-fiber fabrics with the smart textile field; when using specific forms of synthetic fibers –like MRT- and applying electronic monitoring equipment directly on the garment, it is possible to track the reaction of the fibers to the moisture and heat produced by the athlete during exercise and thus help in finding better methods of training, ways to prolong stamina and, in a matter of speaking, manage the power of the muscles. If one takes under consideration that fibers which react to electrical charges are used today, it could also be possible via monitoring the athlete‘s production of sweat and heat to determine muscle fatigue, and consecutively send a small electrical charge to the fibers so that they can expand or contract, thus controlling the flexing of the muscles; this in turn would dramatically increase the comfort of the garment and prevent any muscular injuries caused by athletic activities. It is clear enough that the new breed of high-tech, professional sportswear opens up an entirely new range of possibilities for the textile engineering research of the future.

References

1. Büsgen A., “Shape Weaving – New Invention for producing 3D-Shaped Woven Shells”, Technical Textiles, Melliand International (3), 1995

2. “Fitness Sports News”, http://www.fitnesssports.com, 5/10/2005

3. http://coolmax.invista.com/ why_coolmax.html, 8/10/2005

4. http://www.couloirmag.com/gear/clothing/fabric_glos.asp, 16/10/2005

### 5. http://www.coolmax.invista.com/faqs.html, 12/10/2005

### 6. http://www.golfballs.com/PA1445/Nike-Sphere-Dry-Polo.html, 20/10/2005

### 7. http://www.nike.com.au/running/products/mens/apparel/apparel_tech.cfm, 12/10/2005

### 8. http://www.funkygrad.com/lifestyle/displayarticle.php?artID=525&subcat=wear, 12/10/2005

### 9. http://www.fabriclink.com/pk/Meryl/home.html, 8/10/2005

### 10. http://www.sdy.com/ spectrum_dictionary.pdf, 24/10/2005

### 11.http://www.irc-norddeutschland.de/de/markt/technology-fields/02/database/detail. dtml?ref1=TO-UM-2002-, 24/10/2005

### 12. http://www.fabriclink.com/pk/Meryl_Actisystem/ Home.html, 24/10/2005

### 13. http://www.tactel.com/en/about/tactel_history-nylon.htm, 25/10/2005

# Text boxes

Image-1 Schematics of the Structure of the Coolmax Fiber

The extended surface of the cross-section of the fiber allows the faster sublimation of the moisture

The great gaps amongst the fibers contribute to the fastest movement of the moisture

Schematics of the movement of the moisture across the channels

The great gaps amongst the fibers contribute to the fastest movement of the moisture

The extended surface of the cross-section of the fiber allows the faster sublimation of the moisture

The extended surface of the cross-section of the fiber allows the faster sublimation of the moisture

Image-2 schematics of the function of the Sphere React Dry

Dry= flat shape

Wet= 3-D shape

Image-3  Schematics of the function of the Sphere React Cool

Image-4 Schematics of the function of the Sphere React Pro

Dry=closely woven structure

Wet= sparse structure

Wet= Flat Shape

Wet= 3-D and breathable shape